## Slide 1
ACTIVITY NIGHT
August 24, 2017

## Slide 2
A FOX HUNTING PRIMER
Will not teach you everything you hoped to learn.
Disclaimer
By N1ZN

## Slide 3
Amateur Radio Direction Finding
ARDF
aka Fox Hunting
aka T-Hunting

## Slide 4
Searching for a hidden transmitter
that is transmitting a signal.
It may be continuous transmissions
or intermittent.
What is Fox Hunting or T-Hunting?
The most common band is 2 meter FM.
A common Fox Hunt frequency is 146.565.

## Slide 5
The Hunters can be individuals or teams.
Range can be up to hundreds of miles.
Typically the first to locate the fox.
Variation: the lowest mileage in locating the fox.
Participants
Locations
Winning

## Slide 6
Equipment
Antenna is the key!
Beams - Directivity provides an advantage.
Cubical Quads
Yagis
Polarization is important!

## Slide 7
Dual Antennas
a pair of verticals with a switching device.
Dopplers
typically 4 whip antennas with a ring of leds

## Slide 8
using Handi-Talkies or Scanners
Body Fade or Body Shielding
Move off frequency 5 – 10 KHz
Remove the rubber ducky antenna

## Slide 9
Attenuation
A necessity when very close to the transmitted signal.
Offset attenuator
Third Harmonic
146.565 KHz
X 3 =
439.695 KHz

## Slide 10
Directional Antennas
Popular is the “Tape Measure Antenna”
Yagi made from ½” pvc pipe
Elements made from a 1” tape measure
Simple hair pin match

## Slide 11
WB2HOL Design